## Slide 1: Spectrometry: the basics
Light
Spec
Probe(s)

## Slide 2: Spectrometry: data
Reflectance (relative)
Radiance
Irradiance (vector/scalar)
Transmittance (diffuse/direct)

## Slide 3: Spectrometry: considerations
Greater
- The spec
- Light source
- Light <-> object <-> spec geometry
- Standards
Lesser
- Fibres (diameter/length/sensitivity)
- Filters/collimators/lenses
- Integration time
- Boxcar width/smoothing

## Slide 4: Spectrometry: the spec
Key: sufficient sensitivity across the spectral range
UV – VIS – NIR+
Sensitivity, noise, range
Lots of brands/types
  Oceanview
  Avantes
  Horiba
  StellarNet
  Whatever Jolyon’s invented lately

## Slide 5: Light source
Key: sufficient intensity across the spectral range
Tungsten-Halogen
Deuterium
Xenon Arc Lamps
Light Emitting Diodes (LEDs)
Quartz Tungsten-Halogen (QTH) Lamps
Mercury Arc
...
Typically part of the whole setup, little ongoing consideration
BYO. Very rarely use ‘natural’ light, instead block ambient light and use:

## Slide 6: Geometry
Relationship between light, sample, collector
Need to consider specular (‘mirror’) vs diffuse samples & measurements
Need to take sample measurements under same setup (geometry, distances) as standards

## Slide 7: Standards
Reflectance is a relative measure
Light standards
  Spectralon/teflon (PTFE)
  Barium sulfate
  Mirror (specular standard)
Dark
  Block/unplug collector
  Velvet
Recalibrate regularly to account for light drift, movement etc.

## Slide 8: Other considerations
Hardware
- Fibres
- ~3-500 um common
- Collector/light spot sizes
- Spectral range/sensitivity
- Lenses
Settings
- Integration time
- Boxcar width/smoothing

## Slide 9: In practice
(1) Set up
- set geometry
- collection settings (boxcar, integration...)
(2) Calibrate
- light and dark standardise
(3) Record spectrum